Specific Support Action

DRAGON in support of harmonizing European and Chinese marine
 monitoring for Environment and Security System

Making an inventory of Chinese and European capacities of marine monitoring for environment and security including routine use of Earth observation data.

D2.1: 1st Report on Chinese and European Spaceborne Ocean Observing Systems and Onboard Sensors (1988-2025)

DRAGONESS_D2.1.doc

Project No. 030902

Sixth Framework Programme

Priority GMES: Aeronautics and Space

| Start date of project: 01.09.07 | Duration: 36 months |
| --- | --- |

Authors: Ming-Xia HE, Werner Alpers, Johnny Johannessen, Bertrand Chapron, Shuangyan He, Yunfei Wang, Lei Guan, Jiang Zhu, Junwu Tang, Chuanmin Hu

Abstract

Information on the Chinese and European spaceborne earth observing satellite (and spacecraft) missions between 1988 and 2025 are comprehensively presented, including historical, in-orbit and planned (or future) satellites. A detailed introduction of seven Chinese satellite (and spacecraft) series including FY-n, HY-n, ZY-n, HJ-n, SZ-n, CRS-n and DMC/BJ-1 is given. All above satellite (and spacecraft) series are capable of ocean observation, and therefore comprise the Chinese satellite (and spacecraft) ocean observing system. Furthermore, the satellite (and spacecraft) observing systems for ocean color, sea surface temperature, sea surface height, sea surface vector winds and SAR are listed respectively according to onboard sensors.

The performance of sensors onboard the Chinese and other similar ocean observing satellites is compared and discussed, and the gaps are pointed out. The 21 in-orbit sensors onboard Chinese ocean observing systems and other similar satellite sensors are listed.

The data assimilation into an ENSO prediction system (EPS), the development of a Chinese regional high resolution sea surface temperature system within the framework of GHRSST and the monitoring of floating algae by MODIS data in Qingdao Olympic sailing area in 2008 are introduced. From these three cases, a glance at the status of utilizing Chinese satellite data is given.

- Chinese Spaceborne Ocean Observing Systems

Table 1 shows Chinese spaceborne earth observing satellite missions by launch date, including historical, on-orbit and planned (or future) satellites. There are 7 satellite series in all FengYun satellites (FY-n), ocean satellites (HY-n), resource satellites (CBERS, ZY-n) and environment satellites (HJ-n) are jointly implemented by China National Space Administration (CNSA) and related application sectors which are China Meteorological Administration (CMA), State Oceanic Administration (SOA), Ministry of Land and Resources (MLR) and Ministry of Civil Affairs (MCA) / Ministry of Environmental Protection (MEP) respectively. Shenzhou spacecrafts (SZ-n) and Chinese Remote Sensing satellites (CRS-n or YG-n) are implemented by CNSA. Disaster Monitoring Constellation / BeiJing-1 micro-satellite (DMC / BJ-1 micro-satellite) are implemented by Ministry of Science and Technology of China (MOST). Table 2 outlines the primary sensors and applications of the above six satellite missions and one spacecrafts mission.

FY-n is the meteorological satellite series, including polar-orbiting and geostationary meteorological satellites, whose serial numbers n are odd and even ones respectively. FY-1A and FY-1B are experimental satellites carrying 5-channel Multichannel Visible Infrared Scanning Radiometers (MVISR-1). FY-1C and FY-1D are operational satellites carrying 10-channel Multichannel Visible Infrared Scanning Radiometers (MVISR-2) similar to channels of NOAA/AVHRR and CZCS. FY-3 is the second generation of polar-orbiting meteorological satellites of China carrying 10-channel Visible and InfraRed Radiometer (VIRR, the improved version of MVISR-2), Infrared Atmospheric Sounder (IRAS), MicroWave Temperature Sounder (MWTS), MicroWave Humidity Sounder (MWHS), Solar Backscatter Ultraviolet Sounder (SBUS), Total Ozone Unit (TOU), Earth Radiation Measurement (ERM), Solar Irradiation Monitor (SIM), MicroWave Radiation Imager (MWRI), MEdium Resolution Spectral Imager (MERSI) and Space Environment Monitor (SEM). The first eight sensors are similar to NOAA/AVHRR and TOVS, the MWRI is similar to the TRMM/TMI, and the MERSI is similar to the EOS/MODIS. The SEM measures high-energy particles, high-energy atom, high-energy electrons and radiation dose. FY-3A and FY-3B are experimental satellites. FY-3C, FY-3E and FY-3G are AM satellites, also called FY-3/AM1, FY-3/AM2 and FY-3/AM3. FY-3D, FY-3F and FY-3H are PM satellites, also called FY-3/PM1, FY-3/PM2 and FY-3/PM3. Generally, FY-3 is similar to the American National Polar-orbiting Operational Environmental Satellite System (NPOESS) and the European Meteorological Operational satellite programme (MetOp), however, FY-3 does not carry the active sensors such as Advanced Scatterometer (MetOp/ASCAT), Radar Altimeter (NPOESS/Radar ALT), Aerosol Polarimeter Sensor (NPOESS/APS), GNSS (Global Navigation Satellite System) Receiver for Atmospheric Sounding (MetOp/GRAS) and Atmospheric Laser Doppler instrument (ADM-AEOLUS/ALDIN). FY-2A and FY-2B are also experimental satellites, however, they operated over eight and five years respectively and exceed the two-year design life. The 3-channel Visible and Infrared Spin Scan Radiometers (VISSR-1) are onboard FY-2A and FY-2B. FY-2C and FY-2D are operational satellites carrying Visible and Infrared Spin Scan Radiometer (VISSR-2). The number of spectral channels of VISSR-2 is increased to five, and the infrared wave window 10.5-12.5μm is splited into two channels for the retrieval of Sea Surface Temperature (SST). FY-2E is a substitute satellite for FY-2C, carrying the VISSR-2. FY-2F, FY-2G, FY-2H are the follow-on satellites to FY-2C, FY-2D, FY-2E, and will carry VISSR-n which is the improved version of VISSR-2. FY-4 is the second generation geostationary meteorological satellites of China and consists of two sub-series, optical satellites and microwave satellites. FY-4 optical satellites (FY-4 O) will carry Multiple Channel Scanning Imager (MCSI), Interferometric Infrared Sounder (I I S) and CCD Lightning Mapper (LM). FY-4 O will operate simultaneously in the east and west orbit called FY-4 O EAST and FY-4 O WEST respectively. FY-4 O EAST will provide observation of the middle and eastern China and Pacific Ocean. FY-4 O WEST will provide observation of the western China, Indian Sea, Red Sea and Middle East. FY-4 microwave satellites (FY-4 M) will carry MicroWave Radiation Imager (GEO-MWRI). FY-4 M will operate between FY-4 O EAST and FY-4 O WEST. In general, FY-4 series is similar to American GOES-R satellite and European Meteosat (MTG) satellite, nevertheless, FY-4 does not carry the instruments for space environment detection as GOES-R/SEISS, EXIS and SUVI, and for earth’s geomagnetic field measurement as GOES-R/MAG. In addition, the spatial resolution of optical instruments onboard FY-4 O is lower than GOES-R and Meteosat (MTG).

HY-n is the polar-orbiting ocean satellite series, including three sub-series of ocean color satellites, ocean dynamic environment satellites as well as ocean watch and monitor satellites called HY-1, HY-2 and HY-3 respectively. HY-1A is an experimental satellite and was launched in May 2002. Its operation terminated in April 2004 due to malfunction. HY-1A carried the Chinese Ocean Color and Temperature Scanner (COCTS) and the Coastal Zone Imager (CZI). The COCTS is a 10-channel visible and infrared radiometer similar to ADEOS/OCTS. The CZI is a 4-channel CCD camera. HY-1B is an operational satellite and carries improved COCTS and CZI. The swath of COCTS is increased and the bandwidth of CZI spectral channels is reduced from 80 nm to 20 nm. HY-1C/1D, HY-1E/1F and HY-1G/1H are the follow-on ocean color satellites, and 1C, 1E, 1G and 1D, 1F, 1H are AM and PM satellites respectively. HY-2A is an experimental satellite carrying a Ku-band microwave radiometer, a Ku / C-band microwave altimeter and a 5-channel microwave radiometer similar to QuikSCAT, Topex/Poseidon and EOS-Aqua/AMSR-E, respectively. HY-3 will carry a C-band SAR with 10 m spatial resolution, an X-band SAR with 1 m spatial resolution and an 8-channel CCD imager with 3 m spatial resolution similar to Envisat/ASAR and TerraSAR-X. However, TerraSAR-X has the possibility of sea surface current measurements by along-track interferometry, which is not planned for the HY-3A/SAR-X mission. On the whole, HY-1, 2, 3 series will all go into operation around 2015, and their performance will be equivalent to that of current international operational ocean observing satellites. Some advanced sensors such as EO-1/Hyperion, ISS-JEM/HICO, TerraSAR-X/ATI, Coriolis/WindSat, SMOS, Sentinel-3/SAR-ALT and COMS-1/GOCI, are not flown on HY-n. The ROCASAT-1 satellite was launched by Taiwan before HY-1A and FY-1C satellites, and carried a 6-channel ocean color imager (OCI). Its orbit inclination angle is 35°, and this is the special feature of OCI ocean color data.

#### ZY-n is the polar-orbiting resource satellite series. The governments of China and Brazil signed in 1988 a partnership agreement to fund and develop jointly the China-Brazil Earth-Resources Satellite (CBERS) based on the Chinese ZY-1 satellites scheme: Therefore, CBERS-1, 2, 2B, 3, and 4 belong to the ZY-1 sub-series. The CBERS-1, 2, 2B satellites carry the 5-channel CCD camera, Infrared Multi-Spectral Scanner (IRMSS), Wide Field Imager (WFI) and high resolution camera (HR). The CBERS-2B/CCD & HR with spatial resolution of 20 m and 2 m, respectively, can be used to monitor the coastal ocean. CBERS-3, 4 satellites will carry the improved CCD, IRMSS, WFI and Panchromatic and Multi-spectral camera (PAN-MUX). The performance of CBERS is similar to that of Landsat 7/ETM+ and SPOT 5. ZY-2 satellites are funded and developed by China, and carry high resolution optical sensors (improved HR, PAN-MUX). The performance of ZY-2 is similar to that of QuickBird and IKONOS. The operation time of ZY-2A and ZY-2B greatly exceed their two-year design life, so ZY-2A, ZY-2B and ZY-2C could form an earth observing network.

#### SZ-n is the Chinese manned spacecraft series. SZ-1 flew in space for only one day, and carried out experiments for equipments and data transmission in orbit. SZ-2, 3, 4 flew in space for five to seven days, and the orbital module stayed in orbit for half a year carrying out the experimental observation of the sensors for space and earth environment monitoring. The earth observing sensors included a medium resolution spectral imager, a multi-mode microwave remote sensor, a solar constant monitor, a solar ultraviolet spectral monitor, an atmospheric ozone sounder, an earth radiation budget sensor and so on, which are the payloads of FY-3A and HY-2A. The SZ-5 manned spacecraft flew in space for one day, and the orbital module stayed in orbit for half a year carrying out the experimental observation for space environment monitoring. The SZ-6 manned spacecraft flew in space for 6 days, and the orbital module stayed in orbit for two years carrying out experimental observations for earth environment monitoring. The SZ-7 manned spacecraft is scheduled to be launched in October 2008, and will return after a five-day flight. The astronauts will carry out experiments of the extra-vehicular activity (EVA) and release a micro-satellite carried along with the spacecraft. The orbital module will not stay in orbit as usual.

#### DMC/BJ-1 (Disaster Monitoring Constellation / Beijing -1) is a 166kg small satellite. Three small satellites for earth observation developed by British Surrey Satellite Technology Ltd (SSTL) were successfully launched on 27 September 2003. These three small satellites and the ALSAT-1, a small satellite which was launched by Algeria before, form the international Disaster Monitoring Constellation (DMC). Beijing-1, small satellite (BJ-1) implemented by MOST, was launched on 27 October 2005 and joined in the DMC. The BJ-1 small satellite, also called DMC+4, carries the multi-spectral and panchromatic CCD imagers with the spatial resolution of 32 m and 4 m, respectively. The DMC alliance consists of seven countries, UK, Algeria, China, Turkey, Nigeria, Thailand and Vietnam, and coordinated by SSTL. BJ-1 can also be used for coastal zone monitoring.

#### HJ-n is the polar-orbiting small satellite constellation for environment and disaster monitoring, which consist of ‘2+1’ constellation and ‘4+4’ constellation, called HJ-1 and HJ-2, respectively. HJ-1A and HJ-1B were launched simultaneously. HJ-1A carries a multi-spectral camera (CCD) and a Hyper Spectral Imager (HSI) with a spectral resolution of 5 nm. HJ-1B carries a multi-spectral camera (CCD) and a multi-spectral Infrared Camera (IR). The HSI is similar to ISS-JEM/HICO. HJ-1C will carry an S-band SAR with spatial resolution of 5 m and 20 m similar to the Russian Almaz/SAR. HJ-1 constellation will be very useful for ocean color, ocean dynamic environment and ocean watch and monitoring, and especially the HSI and SAR-S fill the gap of HY-n. HJ-2 constellation will consist of four optical small satellites and four SAR small satellites.

#### CRS-n is a high spatial resolution satellite series, also called YG-n, which carry the high spatial resolution SAR and optical sensors. CRS-1 is the first SAR satellite in China and carries an L-band SAR with a resolution of 5 m. CRS-2 carries optical sensors. CRS-3 carries an L-band SAR with a resolution of 5 m. The launch time of these three satellites is close. CRS-n is very useful for ocean dynamic environment and ocean monitoring.

Table 1: Chinese spaceborne earth observing system (EOS)

Table 2: Primary sensors and applications of Chinese spaceborne EOS

| Satellite series | Satellite | Orbit | Launch date | Design life / EOL date | Primary sensors | Primary applications |
| --- | --- | --- | --- | --- | --- | --- |
| FY-n | FY-1A | Polar | 1988-09-07 | 1988-10 | MVISR-1 | Meteorology |
|  | FY-1B |  | 1990-09-03 | 1991-02 |  |  |
|  | FY-1C |  | 1999-05-10 | 2004-03 | MVISR-2 | Meteorology, Ocean color, SST |
|  | FY-1D |  | 2002-05-15 | 2 years |  |  |
|  | FY-2A | Geostationary | 1997-06-10 | 2006-06 | VISSR-1 | Meteorology, |
|  | FY-2B |  | 2000-06-25 | 2006-06 | VISSR-1 |  |
|  | FY-2C |  | 2004-10-19 | 3 years | VISSR-2 | Meteorology SST |
|  | FY-2D |  | 2006-12-08 | 3 years | VISSR-2 |  |
|  | FY-2E |  | 2008-10 | 3 years | VISSR-2 |  |
|  | FY-2F |  | 2010 | 4 years | VISSR-n |  |
|  | FY-2G |  | 2012 | 4 years | VISSR-n |  |
|  | FY-2H |  | 2014 | 4 years | VISSR-n |  |
|  | FY-3A | Polar | 2008-05-27 | 3 years | VIRR, IRAS, MWTS, MWHS, SBUS, TOU, ERM, SIM, MWRI, MERSI, SEM | Meteorology, Ocean, Land, Space |
|  | FY-3B |  | 2009 | 3 years |  |  |
|  | FY-3C/AM1 |  | 2013 | 3 years |  |  |
|  | FY-3D/PM1 |  | 2015 | 3 years |  |  |
|  | FY-3E/AM2 |  | 2017 | 3 years |  |  |
|  | FY-3F/PM2 |  | 2019 | 3 years |  |  |
|  | FY-3G/AM3 |  | 2021 | 3 years |  |  |
|  | FY-3H/PM3 |  | 2023 | 3 years |  |  |
|  | FY-4 O | Geostationary | 2012 | 4 years | IIS, MCSI, LM(CCD) | Meteorology, Ocean, Land |
|  | FY-4 M |  | 2015 | 4 years | GEO-MWRI |  |
| HY-n | ROCSAT-1 | Polar | 1999-01-27 | 2004-06-16 | OCI, IPEI | Ocean color, Detection of charged particles in the ionosphere |
|  | HY-1A | Polar | 2002-05-15 | 2004-04-01 | COCTS, CZI | Ocean color |
|  | HY-1B |  | 2007-04-11 | 3 years |  |  |
|  | HY-1C/D |  | 2010 | 3 years |  |  |
|  | HY-1E/F |  | 2013 | 3 years |  |  |
|  | HY-1G/H |  | 2016 | 3 years |  |  |
|  | HY-2A |  | 2009 | 4 years | SCA(Ku), ALT(Ku,C), RAD(5 bands) | Ocean dynamic environment |
|  | HY-2B |  | 2012 | 4 years |  |  |
|  | HY-2C |  | 2015 | 4 years |  |  |
|  | HY-2D |  | 2018 | 4 years |  |  |
|  | HY-3A |  | 2012 | 5 years | SAR(X,1m),SAR(C,10m),CCD(3m) | Ocean watch and monitoring |
|  | HY-3B |  | 2017 | 5 years |  |  |
| CBERS, ZY-n | CBERS-1 | Polar | 1999-10-14 | 2003-08-13 | CCD, IRMSS, WFI | Land, Coastal zone |
|  | CBERS-2 |  | 2003-10-21 | 2 years |  |  |
|  | CBERS-2B |  | 2007-09-19 | 2 years | CCD, WFI, HR |  |
|  | CBERS-3 |  | 2009 | 3 years | CCD, IRMSS, WFI, PAN-MUX (PAN-MS) |  |
|  | CBERS-4 |  | 2011 | 3 years |  |  |
|  | ZY-2A | Polar | 2000-09-01 | 2 years | HR, PAN-MS |  |
|  | ZY-2B |  | 2002-10-27 | 2 years |  |  |
|  | ZY-2C |  | 2004-11-06 | 2 years |  |  |
| SZ-n | SZ-1 |  | 1999-11-20 | 1 day |  |  |
|  | SZ-2 |  | 2001-01-10 | 6 days | The orbital module stayed in orbit, Space and earth environment sensor experiments. Such as CMODIS, M3RS, SBUS, TOU, ERM, SIM, etc. |  |
|  | SZ-3 |  | 2002-03-25 | 7 days |  |  |
|  | SZ-4 |  | 2002-12-30 | 5 days |  |  |
|  | SZ-5 |  | 2003-10-15 | 1 day |  |  |
|  | SZ-6 |  | 2005-10-12 | 5 days |  |  |
|  | SZ-7 |  | 2008-10 | 5 days |  |  |
| DMC | DMC/BJ-1 | Polar | 2005-10-27 | 5 years | PAN-MS | Land, Coastal zone |
| CRS-n or YG-n | CRS-1 | Polar | 2006-04-27 | 2 years | L-band SAR | Land, Ocean |
|  | CRS-2 |  | 2007-05-25 | 2 years | HR, PAN-MS |  |
|  | CRS-3 |  | 2007-11-12 | 2 years | L-band SAR |  |
| HJ-n | HJ-1A | Polar | 2008-09-06 | 3 years | CCD, HSI | Environment and disaster monitoring, Ocean |
|  | HJ-1B |  | 2008-09-06 | 3 years | CCD, IR |  |
|  | HJ-1C |  | 2009 | 3 years | S-band SAR |  |
|  | HJ-2 (4+4) |  | 2012 | 3 years | CCD, IR, HSI, SAR |  |

#### All above satellite and spacecraft series are capable of ocean observation, and therefore comprise the Chinese spaceborne ocean observing system. Table 3 to 8 show the satellite and spacecraft missions carrying ocean color sensors, infrared and microwave radiometers, microwave altimeters, microwave scatterometers, microwave SARs and high spatial resolution optical sensors, respectively. In Table 3 to 8, the planned satellite missions are identified by colored bars with black slash and arrows, on-orbit missions are without black slash, and historical missions are without arrows and black slash. Some other ocean observing sensors which are operational and their follow-on are also listed at the bottom of Table 3 to 7, and are identified by gray lines with arrows.

#### Table 3 shows the Chinese satellite missions carrying ocean color sensors. Among seven satellite and spacecraft series, FY-n, HY-n, SZ-n and HJ-n carry ocean color sensors. Thus quasi-simultaneous observation could be achieved with two medium resolution spectral imagers (HY-1B/COCTS, FY-3A/MERSI) and a hyper-spectral imager (HJ-1A/HSI). Together with SeaWiFS, MODIS and its follow-on, MERIS and its follow-on, OCM and its follow-on, Hyperion and its follow-on, and SGLI, quasi-simultaneous observation data from 8-9 ocean color sensors could be obtained. This is very useful for marine ecological environment monitoring such as Red Tides. The key issue is how to get these data quickly and conveniently to the users.

#### Table 4 shows the Chinese satellite missions carrying infrared and microwave radiometers. Among seven satellite and spacecraft series, FY-n and HY-n carry infrared and microwave radiometers which could be used to retrieve Sea Surface Temperature (SST). FY-1D/MVISR-2 and FY-3A/VIRR have three infrared channels. The channels are similar to NOAA/AVHRR, Envisat/AATSR and EOS/MODIS. HY-1B/COCTS has only two infrared channels. FY-3A/MWRI and HY-2A/RAD are 5-channel microwave radiometers. The quasi-simultaneous SST observation could be achieved by FY-1D, FY-3A and HY-1B. Moreover, all-weather and all day/night high resolution SST data could be obtained together with FY-3A/MWRI and HY-2A/RAD. These could contribute to the GHRSST project. Together with AVHRR, MODIS and its follow-on, ATSR and its follow-on, TMI, AMSR-E and its follow-on, and WindSat, the quasi-simultaneous 1 km resolution SST observation data retrieved from 10-11 infrared and microwave radiometers could be obtained. In addition, Chinese geostationary satellites (FY-2C, 2D, 2E/VISSR-2, FY-4/MCSI, GEO-MWRI), and other geostationary satellites (GOES/IMAGER, Meteosat/MVIRI), could provide high temporal resolution average cloud-free SST.

#### Table 5 shows the Chinese satellite missions carrying microwave altimeters. Among seven satellite and spacecraft series, only HY-n carries a microwave altimeter (ALT). HY-2A, the first satellite carrying the ALT in China, will be launched in 2009. The dual-frequency (Ku, C) altimeter is similar to Topex/Poseidon. HY-2A/ALT will operate in orbit concurrently with Jason-1, 2, 3, Envisat/ALT, CryoSat-2/SIRAL, Sentinel/SRAL and NPOESS/ALT, so data from 4-5 altimeters could be obtained for the inter-comparison and merging of the data.

#### Table 6 shows the Chinese satellite missions carrying microwave scatterometers. Among seven satellite and spacecraft series, only the HY-n carries a microwave scatterometer (SCAT). HY-2A, the first satellite carrying a scatterometer (SCAT) in China, will be launched in 2009. The SCAT will operate at Ku frequency similar to QuikSCAT. HY-2A/SCAT will operate in orbit concurrently with QuikSCAT, ERS-2/SACT, Coriolis/WindSat, MetOp/ASCAT, OceanSat-2/SCAT, GCOM/SeaWinds, NPOESS /CMIS, so data from 4-5 sactterometers could be obtained for data inter-comparison and data merging. WindSat is a full polarization microwave radiometer, and can provide sea surface vector winds. Furthermore, the microwave radiometers and microwave altimeters listed in Tab.4 and Tab.5 could provide sea surface wind speed. Microwave SARs listed in Tab.7 could provide high spatial resolution sea surface vector winds.

#### Table 7 shows the Chinese satellite missions carrying microwave SARs. Among seven satellite and spacecraft series, CRS-n, HJ-n and HY-n carry microwave SARs. CRS-1/SAR (L), the first SAR satellite in China, was launched on 27 April 2006, and its sister satellite CRS-3/SAR (L) was launched on 12 November 2007. HJ-1C/SAR (S) will be launched in 2009. HY-3A 3B/SAR (X, C) will be launched after 2012. If these SAR satellites could operate over design life, then multi-frequency SARs will be in orbit concurrently. Together with ERS & Envisat/SAR (C) and their follow-on, TerraSAR-X and its follow-on, COSMO-SkyMed/SAR (X) and its follow-on, RADARSAT-1/SAR (C) and its follow-on, and ALOS/PALSAR (L), there will be 8-9 SAR sensors operating in orbit concurrently. However, it is relatively inconvenient to obtain SAR data.

#### Table 8 shows the Chinese satellite missions carrying high spatial resolution optical sensors. Among seven satellite and spacecraft series, HY-n, ZY-n, HJ-n and DMC/BJ-1 carry optical sensors with spatial resolution better than 30 m as follows, which could be used for qualitative observation and monitoring of coastal zone and analysis of coastal SAR images.

| Optical sensors HY-3A, 3B/CCD | Spatial resolution 3 m |
| --- | --- |
| ZY-2A, 2B, 2C/HR, PAN-MS | 2 m, 5 m |
| CBERS-1, 2/CCD | 20 m |
| CBERS-2B/ CCD, HR | 20 m, 2 m |
| CBERS-3, 4/ PAN-MUX | 10 m, 2 m |
| HJ-1A, 1B/CCD | 30 m |
| HJ-2 (4)/CCD | < 30 m |
| DMC/BJ-1/PAN-MS | 32 m, 4 m |

Table 3: Chinese satellite missions carrying ocean color sensors

Table 4: Chinese satellite missions carrying infrared and microwave radiometers

Table 5: Chinese satellite missions carrying microwave altimeters

Table 6: Chinese satellite missions carrying microwave scatterometers

Table 7: Chinese satellite missions carrying microwave SARs

Table 8: Chinese satellite missions carrying high spatial resolution optical sensors

- European Spaceborne Ocean Observing Systems

The European Spaceborne Earth Observing System consists of ESA satellites and national satellites.

2.1. European Spaceborne Ocean Observing Systems handled by ESA

Table 9 shows European earth observing satellite missions handled by ESA including historical, in-orbit and planned (or future) satellites. The European Remote Sensing satellites ERS-1 and ERS-2 have been launched in 1991 and 1995, respectively, the Envisat satellite in 2002, and the METOP satellite in 2006 (26 October 2006).

Table 9: Present and Future European Spaceborne Ocean Observing Systems

The sensors onboard the satellites which are used for ocean observations are the following:

- On ERS-1 and ERS-2: An Active Microwave Instrument (AMI) comprising a C-band scatterometer and a C-band SAR, an altimeter, and an Along Track Scanning Radiometer (ATSAR).

- On Envisat: An Advanced C-band SAR (ASAR), an altimeter, an Advanced Along Track Scanning Radiometer (AATSR), and a medium-spectral resolution, imaging spectrometer (MERIS).

- On METOP: An Advanced Scatterometer (ASCAT).

The parameters of these sensors can be found in the tables in the next section, where the performances of existing and future sensors on Chinese satellites are compared with those on European and non-European satellites:

- Table 16: ERS-1/2 and METOP scatterometers

- Table 17: Envisat ASAR

- Table 15: Envisat altimeter

- Table 13: Envisat AATSR

- Table 12: Envisat MERIS

METOP is Europe's first polar-orbiting satellite dedicated to operational meteorology. It represents the European contribution to a co-operative venture with the United States providing data to monitor climate and improve weather forecasting. The METOP series consists of a total of three satellites, which are designed to provide meteorological operational data from polar orbit until 2020.

METOP carries an Advanced Scatterometer (ASCAT) for measuring wind speed and direction over the ocean. It is an enhanced follow-on instrument to the scatterometers flown on ESA's ERS-1 and ERS-2 satellites. It has six antennas which allows for simultaneous coverage of two swaths on either side of the satellite ground track, providing twice the information of the earlier instruments on ERS-1 and ERS-2 (see Table 16). Sea surface wind speed is used, among others, as input in wave forecast models. If the Quikscat mission should come to an end (Quikscat was launched already in 1999), METOP can fill the gap. Thus continuity of global sea surface wind measurements is provided by the three METOP satellites until 2020.   
Starting in 2011, Europe plans to start a series of earth observation satellites called the “Sentinal series”. The Sentinel satellites will be part of the European project “Global Monitoring for Environment and Security (GMES)”. GMES is a joint initiative of ESA and the European Union “to respond to the need to establish a European capacity for Global Monitoring of Environment and Security to support the public policy maker’s need for global access to reliable, accurate and up-to-date information on issues of environment and security”, It will be the European contribution to the Global Earth Observation System of Systems (GEOSS).

Five different types of satellites are planned in the Sentinel series, called Sentinel 1- 5. Each type consists of several satellites. Their characteristics are given in Table 10.

Table 10:  Future European Spaceborne Earth Observing Missions: the Sentinel satellites

The Sentinel satellites are designed to provide continuity of the ERS, ENVISAT, SPOT missions, Sentinel 1 and Sentinel 3 will be used for ocean monitoring.

Sentinal 1 will carry the European Radar Observatory, which is a C-band Synthetic Aperture Radar (same frequency as Radarsat 2) and has an Interferometric Wide Swath mode. It measures sea surface winds, currents and waves, and will be used in oil spill information services and ship detection services for fisheries and security. Three Sentinel 1 satellites will be launched (in 2011, 2012, and 2003) such that coastal zones and the main shipping routes are covered on a daily basis. The parameters of the Sentinel-1 SAR are given in Table 11.

Table 11: Sentinel-1 SAR image quality

Sentinel 3 carries an advanced radar altimeter and two multi-channel optical radiometers (VIS, IR) for measuring ocean colour and sea surface temperature. The Ocean and Land Colour Instrument (OLCI) has a strong heritage from MERIS instrument on Envisat, the Sea and Land Surface Temperature Radiometer (SLSTR), a strong heritage from AATSR instrument on Envisat, and the SAR Radar Altimeter (SRAL) a strong heritage from Cryosat (an ESA satellite to be launched in 2009). The first of 3 Sentinel 3 satellites will be launched in 2013.

2.2. European National Spaceborne Ocean Observing Systems

An example of a national Earth Observing satellite system is the French SPOT satellite series. However, it has only limited application for monitoring the ocean. In 2007 three national European satellites were launched which have great potential for ocean monitoring: the German satellite TerraSAR-X (on 15 June 2007) and two Italian/French COSMO-SkyMed satellites (on 8 June and 9 December 2007). Both carry high-resolution X-band SARs. The parameters of TerraSAR-X can be found in Table 17 of the next section. The parameters of the SAR onboard COSMO-SkyMed are quite similar. Like TerraSAR-X, also COSMO-SkyMed SAR has also spotlight mode with a resolution of 1 m. COSMO-SkyMed (Constellation of Small Satellites for Mediterranean basin Observation) consists of a constellation of 4 Synthetic Aperture Radar satellites for primarily military surveillance. But products will be made available also to civilian users.

- Comparison of Chinese and other international sensors for ocean observation

#### Table 12 to 17 shows the comparison of Chinese and other sensors including ocean color sensors, sea surface temperature sensors, microwave radiometers, microwave altimeters, microwave scatterometers, and microwave SARs, respectively.

#### Table 12 shows a comparison of different ocean color sensors. The comparison of HY-1B/COCTS with SeaWiFS shows that they have similar visible spectral bands and bandwidth. The former has two infrared bands and the latter has better radiometric accuracy. The comparison of HY-3A/MERSI with MODIS shows that they have similar visible and near-infrared spectral bands. The latter has better bandwidth of visible bands and radiometric accuracy, while the former has larger swath. Relatively, MERIS is the optimal ocean color sensor by comparison of spectral bands, bandwidth, SNR, radiometric accuracy and spatial resolution. The following is the comparison of hyper spectral imagers which are not included in Tab. 12.

| Hyper spectral imager | Spectral range | Band number | Bandwidth | Spatial resolution | Swath |
| --- | --- | --- | --- | --- | --- |
| HJ-1A/HSI | 0.45-0.95 μm | 128 | 5 nm (average) | 100 m | 50 km |
| EO-1/Hyperion | 0.4-1.0 μm 0.9-2.5 μm | 220 | 10nm | 30 m | 7.5 km |
| ISS-JEM/HICO | 0.38-1.0 μm | 124 | 5 nm | 100 m | 50 km |

#### Table 13 shows comparison of infrared sensors which are used to retrieve SST. FY-3A/VIRR, AVHRR, AATSR and MODIS all have three infrared channels of 3.7 μm, 11 μm and 12 μm, and MODIS has two ancillary infrared channels of 4.0μm and 4.1μm. HY-1B/COCTS has only two infrared channels of 11 μm and 12 μm. The radiometric accuracy of HY-1B/COCTS and FY-3A/VIRR is lower than AATSR and MODIS, and the noise equivalent temperature difference (NEΔT) is worse than AATSR, MODIS and AVHRR too. Relatively, MODIS has the optimal infrared channels to retrieve SST by comparison of infrared spectral bands, bandwidth, NEΔT, radiometric accuracy and swath.

#### Table 14 shows comparison of microwave radiometers which are used to retrieve SST and sea surface wind speed (or sea surface vector winds). Compared FY-3A/MWRI with TMI, they have similar frequency and polarization. The latter has better NEΔT and spatial resolution, while the former has larger swath. Compared HY-2/RAD with AMSR-E, they have similar frequency (except 89GHz), polarization and NEΔT, while the latter has better spatial resolution. WindSat has similar frequencies to AMSR-E and HY-2/RAD for retrieval of SST, and the more important is that it could be used to retrieve sea surface vector winds due to full polarization.

#### Table 15 shows comparison of microwave altimeters. The frequency of HY-2A/ALT is similar to that of Topex/Poseidon, while HY-2A/ALT has the lower spatial resolution, longer repeat cycle and lower sea-level measurement accuracy.

#### Table 16 shows comparison of microwave scatterometer. The frequency, polarization, swath and wind speed accuracy of HY-2A/SCAT are similar to those of QuikSCAT, and HY-2A/SCAT has lower spatial resolution, longer repeat cycle and larger wind speed range.

#### Table 17 shows comparison of microwave SARs. HY-3A/SAR (X) and TerraSAR-X have similar operation modes and spatial resolution. The former has larger swath and incidence angle, while the latter has more polarization modes, shorter repeat cycle and the along track InSAR operation mode. HY-3A/SAR (C) and Envisat/ASAR have similar operation modes and spatial resolution. The former has larger swath and incidence angle. The latter’s alternating polarization mode is based on the image mode. HJ-1C/SAR only has two operation modes and two polarizations, and has similar spatial resolution, swath and incidence angle to TerraSAR-X.

|  | HY-1B/COCTS | FY-3A/MERSI | Envisat/MERIS | EOS/MODIS | OrbView-2/SeaWiFS |
| --- | --- | --- | --- | --- | --- |
| Launch Agency | CNSA SOA | CNSA CMA | ESA | NASA | NASA |
| Orbit | polar, 798km, 98.8deg, 10:30±30min (D) | polar, 836km, 98.75deg, 10:00-10:20 (D) | polar, 800 km, 98.55deg, 10:00 (D) | polar, 705 km, 98.2deg, 10:30 (D, Terra) or 13:30 (A, Aqua) | polar, 705km, 98.2deg, 12:00 (D) |
| Swath | 3100km | 3200km | 1150km | 2330 km | 2801km |
| Quantization | 10 bits | 12 bits | 16 bits | 12 bits | 10 bits |
| Spatial Resolution | 1100m | 250m (bands 1-5) 1000m (bands 6-20) | 300m/1200m (all bands) | 250 m (bands 1-2), 500 m (bands 3-7), 1000 m (bands 8-36) | 1100m |
| Radiometric Accuracy | 10% (bands 1-8) | 7% (bands 1-4, 6-14) 10% (bands 15-20) | < 4% | 5% (bands 1-19, 26) 1% (bands 20-25, 27-36) | < 5% |
| SNR, NEΔρ, NEΔT | SNR Band 1, 440; 2, 600; 3, 590; 4, 560; 5, 525; 6, 390; 7, 400; 8, 415 | NEΔρ Band 1, 0.45%; 2-3, 0.4%; 4, 0.45%; 6-7, 0.1%; 8-14, 0.05% | SNR (typical) 1700 | SNR Band 1, 128; 2, 201; 3, 243; 4, 228; 8, 880; 9, 838; 10, 802; 11, 754; 12, 750; 13, 910; 14, 1087; 15, 586; 16, 516 | SNR Band 1, 499; 2, 674; 3, 667; 4, 640; 5, 596; 6, 442; 7, 455; 8, 467 |
| Bands | 1 412 nm, 20 nm 2 443 nm, 20 nm 3 490 nm, 20 nm 4 520 nm, 20 nm 5 565 nm, 20 nm 6 670 nm, 20 nm 7 750 nm, 20 nm 8 865 nm, 40 nm 9 10350 nm, 100 nm 10 11950 nm, 1100 nm | 6 412 nm, 20 nm 7 443 nm, 20 nm 1 470 nm, 50 nm 8 490 nm, 20 nm 9 520 nm, 20 nm 2 550 nm, 50 nm 10 565 nm, 20 nm 11 650 nm, 20 nm 3 650 nm, 50 nm 12 685 nm, 20 nm 13 765 nm, 20 nm 14 865 nm, 20 nm 4 865 nm, 50 nm 15 905 nm, 20 nm 16 940 nm, 20 nm 17 980 nm, 20 nm 18 1030 nm, 20 nm 19 1640 nm, 50 nm 20 2130 nm, 50 nm 5 11250 nm, 2500 nm | 1 412 .5 nm, 10 nm 2 442.5 nm, 10 nm 3 490 nm, 10 nm 4 510 nm, 10 nm 5 560 nm, 10 nm 6 620 nm, 10 nm 7 665 nm, 10 nm 8 681.25 nm, 7.5 nm 9 708.75 nm, 10 nm 10 753.75 nm, 7.5 nm 11 760.625 nm, 3.75 nm 12 778.75 nm, 15 nm 13 865 nm, 20 nm 14 885 nm, 10 nm 15 900 nm, 10 nm | 8 412 nm, 15 nm 9 443 nm, 10 nm 3 469 nm, 20 nm 10 488 nm, 10 nm 11 531 nm, 10 nm 12 551 nm, 10 nm 4 555 nm, 20 nm 1 645 nm, 50 nm 13 667 nm, 10 nm 14 678 nm, 10 nm 15 748 nm, 10 nm 2 858 nm, 35 nm 16 870 nm, 10 nm 17 905 nm, 30 nm 18 936 nm, 10 nm 19 940 nm, 25 nm 5 1240 nm, 20 nm 26 1375 nm, 30 nm 6 1640 nm, 24 nm 7 2130 nm, 50 nm | 20 3750 nm, 180 nm 21 3959 nm, 60 nm 22 3959 nm, 60 nm 23 4050 nm, 60 nm 24 4466 nm, 65 nm 25 4515 nm, 67 nm 27 6715 nm, 360 nm 28 7325 nm, 300 nm 29 8550 nm, 300 nm 30 9730 nm, 300 nm 31 11030 nm, 500 nm 32 12020 nm, 500 nm 33 13335 nm, 300 nm 34 13635 nm, 300 nm 35 13935 nm, 300 nm 36 14235 nm, 300 nm | 1 412 nm, 20 nm 2 443 nm, 20 nm 3 490 nm, 20 nm 4 510 nm, 20 nm 5 555 nm, 20 nm 6 670 nm, 20 nm 7 765 nm, 40 nm 8 865 nm, 40 nm |

Table 12: Comparison of ocean color sensors

|  | HY-1B/COCTS | FY-3A/VIRR | Envisat/AATSR | EOS/MODIS | NOAA-N/AVHRR |
| --- | --- | --- | --- | --- | --- |
| Launch Agency | CNSA SOA | CNSA CMA | ESA | NASA | NOAA |
| Orbit | polar, 798km, 98.8deg, 10:30±30min (D) | polar, 836km, 98.75deg, 10:00-10:20 (D) | polar, 800 km, 98.55deg, 10:00 (D) | polar, 705 km, 98.2deg, 10:30 (D, Terra) or 13:30 (A, Aqua) | polar, 854km, 98.74deg, 13:37 (A) |
| Swath | 3100km | 2900km | 500km | 2330 km | 2900km |
| Quantization | 10 bits | 10 bits | 12 bits | 12 bits | 10 bits |
| Spatial Resolution | 1.1km | 1.1km | 1km | 1km (bands 8-36) | 1.1 km |
| Radiometric Accuracy | 1K@300K (bands 9-10) | 1K@270K (band 3-5) | better than 0.5 K (absolute, 50×50 km), better than 0.1 K (relative, 1×1km) | 1% (bands 20-25, 27-36, absolute) | Traceable to NIST |
| SNR, NEΔρ, NEΔT | NEΔT Band 9-10, 0.2K@300K | NEΔT Band 3, 0.3K@300K; 4-5, 0.2K@300K | NEΔT Band 5, 0.08K@270K; 6-7, 0.05K@270K | NEΔT Band 20, 31-32, 0.05K@300K 22-23, 0.07K@300K | NEΔT Band 3B-5, 0.12 K @ 300K |
| Bands | 1 412 nm, 20 nm 2 443 nm, 20 nm 3 490 nm, 20 nm 4 520 nm, 20 nm 5 565 nm, 20 nm 6 670 nm, 20 nm 7 750 nm, 20 nm 8 865 nm, 40 nm 9 10.3-11.4 µm 10 11.4-12.5 µm | 7 455 nm, 50 nm 8 505 nm, 50 nm 9 555 nm, 50 nm 1 630 nm, 100 nm 2 865 nm, 50 nm 10 1.360 µm, 0.07 µm 6 1.600 µm, 0.09 µm 3 3.55-3.85 µm 4 10.3-11.3 µm 5 11.5-12.5 µm | 1 555 nm, 20 nm 2 659 nm, 20 nm 3 865 nm, 20 nm 4 1610 nm, 300 nm 5 3.55-3.85 µm 6 10.35-11.35 µm 7 11.50-12.50 µm | 8 412 nm, 15 nm 9 443 nm, 10 nm 3 469 nm, 20 nm 10 488 nm, 10 nm 11 531 nm, 10 nm 12 551 nm, 10 nm 4 555 nm, 20 nm 1 645 nm, 50 nm 13 667 nm, 10 nm 14 678 nm, 10 nm 15 748 nm, 10 nm 2 858 nm, 35 nm 16 870 nm, 10 nm 17 905 nm, 30 nm 18 936 nm, 10 nm 19 940 nm, 25 nm 5 1240 nm, 20 nm 26 1375 nm, 30 nm 6 1640 nm, 24 nm 7 2130 nm, 50 nm | 20 3.66-3.84 µm 21 3959 nm, 60 nm 22 3959 nm, 60 nm 23 4050 nm, 60 nm 24 4466 nm, 65 nm 25 4515 nm, 67 nm 27 6715 nm, 360 nm 28 7325 nm, 300 nm 29 8550 nm, 300 nm 30 9730 nm, 300 nm 31 10.78-11.28 µm 32 11.77-12.27 µm 33 13335 nm, 300 nm 34 13635 nm, 300 nm 35 13935 nm, 300 nm 36 14235 nm, 300 nm | 1 630 nm, 100nm 2 862 nm, 275 nm 3A 1.58-1.64 µm 3B 3.55-3.93 µm 4 10.3-11.3 µm 5 11.5-12.5 µm |

Table 13: Comparison of Infrared sensors

|  | HY-2/RAD | FY-3A/MWRI | EOS-Aqua/AMSR-E | TRMM/TMI | Coriolis/WindSat |
| --- | --- | --- | --- | --- | --- |
| Launch Agency | CNSA SOA | CNSA CMA | NASA JAXA | NASA JAXA | NRL AFRL |
| Orbit | Polar, 963/965km, 99.3deg, 6:00 or 18:00 (D) | Polar, 836km, 98.75deg, 10:00-10:20 (D) | Polar, 705 km, 98.2deg, 13:30 (A) | Polar, non-sun-synchronous, 402km, 35deg | Polar, 840 km,98.7deg, 17:59 (A) |
| Swath | 1600km | 1400km | 1450km | 878km | 1000km |
| Center Frequency , Bandwidth , Polarization | Band 1-2, 6.6 GHz, 350MHz, VH; 3-4, 10.7GHz, 250MHz, VH; 5-6, 18.7GHz, 250MHz, VH; 7, 23.8GHz, 400MHz, V; 8-9, 37GHz, 1000MHz, VH | Band 1-2, 10.65GHz, 180MHz, VH; 3-4, 18.7GHz, 200MHz, VH; 5-6, 23.8GHz, 400MHz, VH; 7-8, 36.5GHz, 900MHz, VH; 9-10, 89 GHz, 2×2300MHz, VH; | Band 1-2, 6.925 GHz, 350MHz, VH; 3-4, 10.65GHz, 100MHz, VH; 5-6, 18.7GHz, 200MHz, VH; 7-8, 23.8GHz, 400MHz, VH; 9-10, 36.5GHz, 1000MHz, VH 11-12, 89.0GHz, 3000MHz, VH | Band 1-2, 10.65GHz, 100MHz, VH; 3-4, 19.35GHz, 500MHz, VH; 5, 21.3GHz, 200MHz, V; 6-7, 37.0GHz, 2000MHz, VH; 8-9, 85.5GHz 3000MHz VH | Band 1-2, 6.8GHz, 125MHz, VH; 3-8, 10.7GHz, 300MHz, V H ±45 L R; 9-14, 18.7GHz, 750MHz, V H ±45 L R; 15-16, 23.8GHz, 500MHz, V H; 17-22, 37.0GHz, 2000MHz, V H ±45 L R; |
| NEΔT | 1-7 0.5K 8-9 0.8K | 1-2 0.6K; 3-8 1K; 9-10 2K | 1-2 0.34K; 3-6 0.7K; 7-8 0.6K; 9-10 0.7K; 11-12 1.2K | 1 0.63K; 2 0.54K; 3 0.50K; 4 0.47K; 5 0.71K; 6 0.36K; 7 0.31K; 8 0.52K; 9 0.93K | 1-2 0.63K; 3-14 0.44K; 15-16 0.60K; 17-22 0.42K |
| IFOV | 1-2 100km; 3-4 62km; 5-6 36km; 7 30km; 8-9 18km | 1-2 51 x 85 km; 3-4 30 x 50 km; 5-6 27 x 45 km; 7-8 18 x 30 km; 9-10 9 x 15 km | 1-2 43 x 75 km 3-4 29 x 51 km 5-6 16 x 27 km 7-8 18 x 32 km 9-10 8.2 x 14.4 km 11 3.7 x 6.5 km 12 3.5 x 5.9 km | 1-2 37 x 63 km 3-4 18 x 30 km 5 18 x 23 km 6-7 9 x 16 km 8-9 5 x 7 km | 1-2 40 x 60 km; 3-8 25 x 38 km; 9-14 16 x 27 km; 15-16 12 x 20 km; 17-22 8 x 13 km |
| Pixel |  |  | 1-10 9 x 10 km 11 4.5 x 4 km 12 4.5 x 6 km | 1-7 9.1 x 13.9 km 8-9 4.6 x 13.9 km | 1-2 40 x 50 km; 3-8 20 x 25 km; 9-14 10 x 25 km; 15-16 10 x 12.5 km; 17-22 5 x 12.5 km |
| Incidence Angle | 40 deg | 53 deg | 1-11 55 deg; 12 54.5 deg | 53 deg | 1-2 53.5 deg; 3-8 49.9 deg; 9-14 55.3 deg; 15-22 53.0 deg; |

Table 14: Comparison of microwave radiometers

Table 15: Comparison of microwave altimeters

|  | HY-2A/ALT | Envisat/ALT | Topex/Poseidon | Jason-1 | CryoSat |
| --- | --- | --- | --- | --- | --- |
| Launch Agency | CNSA SOA | ESA | NASA CNES | NASA CNES | ESA |
| Orbit | Polar, 963km, 99.3 deg | Polar, 800 km, 98.55 deg | Polar,non-sun-synchronous, 1336km, 66deg | Polar,non-sun-synchronous, 1336 km, 66 deg | Polar,non-sun-synchronous, 717 km, 92 deg |
| Repeat Cycle (days) | 14/168 | 35 | 10 | 10 | 369 (30 day sub-cycle) |
| Emitted Frequency (GHz) | Ku, 13.58 C, 5.25 | Ku, 13.575 S, 3.2 | Ku, 13.6 C, 5.3 | Ku, 13.575 C, 5.3 | Ku, 13.575 (LRM, SAR, SARIn) |
| Bandwidth (MHz) | 320, 80, 20 (Ku) 320, 160 (C) | 320, 80, 20 (Ku） 160 (S) | 320 (Ku) 320, 100 (C) | 320 (Ku, C) | 350 (Ku) |
| Spatial resolution (km) | 16 | 8 | 6 | 6 | 0.25 |
| Altimeter Accuracy (cm) | 5-8 | 4.5 | 4.2 | 3.3 | 1.6-2.7 |

|  | HY-2A/SCAT | ERS-2/SCAT | QuikSCAT | MetOp-A/ASCAT | GCOM W2 W3/SeaWinds |
| --- | --- | --- | --- | --- | --- |
| Launch Agency | CNSA SOA | ESA | NASA | ESA | JAXA NASA |
| Orbit | Polar, 963/965 km 99.3deg, 18:00 (D) | Polar, 785 km 98.5deg, 10:30 (D) | Polar, 803 km 98.6 deg, 6:00 (D) | Polar, 817 km 98.7 deg, 09:30 (D) | Polar, 699.6 km 98.19 deg, 13:30 (D) |
| Repeat Cycle | 14/168 days | 35 days | 4 days | 29 days |  |
| Frequency | Ku | C | Ku | C | Ku |
| Polarization | HH VV | VV | HH VV | VV | HH VV |
| Spatial Resolution | 50 km | 25 km, 50 km | 25 km | 50 km | 12.5 km, 25 km, 50 km |
| Swath | >1350 km（HH） >1700 km（VV） | 500 km | 1400 km（HH） 1800 km（VV） | 550 km*2 | 1400 km（HH） 1800 km（VV） |
| Incidence Angle | 38 deg & 44 deg | 18deg～59deg | 46deg & 54deg | 45～65deg | 46deg & 54deg |
| Wind Speed Range | 2～24 m/s | 4～24 m/s | 3～30 m/s | 4～24 m/s | 3～30 m/s |
| Wind Speed Accuracy | 2 m/s, 10% | 2 m/s | 2 m/s | 2 m/s, 10% | 2 m/s |
| Wind Direction Accuracy | 20 deg | 20 deg | 20 deg | 20 deg | 20 deg |

Table 16: Comparison of microwave scatterometers

|  | HJ-1C/SAR | HY-3A.B/SAR | TerraSAR-X/SAR | Envisat/ASAR | Radarsat-2/SAR |
| --- | --- | --- | --- | --- | --- |
| Launch Agency | CNSA MCA/MEA | CNSA SOA | DLR | ESA | CSA |
| Orbit | Polar，500km 97.37deg 6:00AM (D) | Polar，799.9 Km 98.48 6:00AM (D) | Polar，514.8km 97.44 deg 18:00PM (D) | Polar，800 km 98.55 deg 10:00AM (D) | Polar，789 km 98.6 deg 6:00AM (D) |
| Repeat Cycle | 31days | 29days | 11days | 35days | 24days |
| NESZ |  | <-20dB | -16～-23dB | -19～-35dB | -22～-30dB |
| Rad. accur. | 3dB | <1.5dB | 1～3.1dB | 1.5～3.5dB | <1dB |
| Frequency | S-band | X-band | C-band | X-band | C-band | C-band |
| Operation mode， Resolution (m)， Swath (km)， Polarization， Incidence Angle (deg) | Stripmap, 5，40， VV or HH, 31～44 ScanSAR, 20，100， VV or HH, 31～44 | Precise mode, 1，20～40, HH VV， 15～60 Strip mode， 5，60～80， HH VV， 15～60 ScanSAR， 10，120～150， HH VV， 15～60 | Wave mode, 10, 5, HH+VV or HH+HV or VV+VH, 15~60 Image mode， 25，150， HH+VV or HH+HV or VV+VH, 15～60 Wide swath mode， 100，650， HH+VV or HH+HV or VV+VH, 15～60 Global monitoring, 1000，650， HH+VV or HH+HV or VV+VH, 15～60 | Spotlight， 1～2，10， HH+VV or HH+HV or VV+VH, 20～55 Stripmap， 3～6，30， HH+VV or HH+HV or VV+VH， 20～45 ScanSAR， 16，100, HH+VV or HH+HV or VV+VH, 20～45 Dual Receive Antenna Mode, 300 MHz Mode | Wave mode， 30，5， HH or VV， 15～45 Image mode， 30，56～100， HH or VV， 15～45 Alternating Polarization mode， 30，100， VV+HH or HV+HH or VH+VV， 15～45 Wide Swath mode， 150，400， HH or VV， 15～37 Globe Monitoring mode， 1000，400， HH or VV， 15～37 | Ultra-Fine， 3(Range)*3(Azimuth)，20， HH or HV or VV or VH，30～49 Multi-Look Fine， 8(Range)*8(Azimuth)，50， HH or HV or VV or VH，30～50 Fine， 8(Range)*8(Azimuth)，50， HH or HV or VV or VH or HH+HV or VV+VH，30～50 Fine Quad-Pol， 12(Range)*8(Azimuth)25,HH+HV+VV+VH，20～41 Standard Quad-Pol, 25(Range)*8(Azimuth)25,HH+HV+VV+VH，20～41 Extended High， 18(Range)*26(Azimuth)，75， HH or HV or VV or VH，49～60 Standard， 25(Range)*26(Azimuth)，100， HH or HV or VV or VH or HH+HV or VV+VH，20～49 Wide， 30(Range)*26(Azimuth)，150， HH or HV or VV or VH or HH+HV or VV+VH ，20～45 ScanSAR Narrow， 50(Range)*50(Azimuth)，300， HH or HV or VV or VH or HH+HV or VV+VH ，20～46 ScanSAR Wide， 100(Range)*100(Azimuth)，500， HH or HV or VV or VH or HH+HV or VV+VH ，20～49 |

Table 17: Comparison of microwave SARs

#### As mentioned above, there are in 2008 at least 21 Chinese sensors for ocean monitoring in orbit. These Chinese satellite sensors and other international satellite sensors are listed as follows. It shows that the number of microwave sensors and active sensors are less than optical sensors.

| Chinese satellite sensors | Retrieval parameters | Similar sensors |
| --- | --- | --- |
| FY-1D / MVISR-2 | Ocean Color, SST | AVHRR, CZCS |
| FY-2C / VISSR-2 | SST | GOES / IMAGER |
| FY-2D / VISSR-2 | SST | GOES / IMAGER |
| FY-3A / VIRR | Ocean Color, SST | AVHRR, CZCS |
| FY-3A / MERSI | Ocean Color | MODIS |
| FY-3A / MWRI | SST, Wind speed | TMI |
| HY-1B / COCTS | Ocean Color, SST | OTCS, SeaWiFS |
| CRS-1 / SAR (L) | Ocean |  |
| CRS-3 / SAR (L) | Ocean |  |
| HJ-1A / HSI | Ocean Color | Hyperion, HICO |
| HJ-1B / CCD | Coastal Zone | Landsat 7 / ETM+ |
| CBERS-2 / CCD | Coastal Zone | Landsat 7 / ETM+, SPOT 5 |
| CBERS-2B / CCD, HR | Coastal Zone | Landsat 7 / ETM+, SPOT 5 QuickBird |
| ZY-2A / PAN-MS, HR | Coastal Zone | QuickBird, IKONOS |
| ZY-2B / PAN-MS, HR | Coastal Zone | QuickBird, IKONOS |
| ZY-2A / PAN-MS, HR | Coastal Zone | QuickBird, IKONOS |
| DMC-BJ 1 / PAN-MS | Coastal Zone | Landsat 7 / ETM+ |

4．Three cases of utilizing satellite data in China

#### Data assimilation into ENSO ensemble prediction system (EPS)

#### The ENSO EPS of Institute of Atmospheric Physics routinely use the satellite altimeter and SST products for initialization (Zhang et al, 2006, 2007, 2008). The SST data used in EPS is the improved monthly extended reconstructed SST (ERSST.v3) by Smith et al. (2008), with 2° horizontal resolution. The global SST data can be automatically downloaded on the third day of each month via the anonymous ftp site (ftp://eclipse.ncdc.noaa.gov/pub/ersst/netcdf/), and the data domain is configured to the tropical Pacific Ocean. The observed SL anomaly data used in the EPS is from the gridded AVIOS Ssalto/Duacs multi-mission altimeter products with 1° horizontal resolution. The daily data is available on the anonymous ftp site: ftp://ftp.cls.fr/pub/oceano/AVISO/SSH/duacs/global/nrt/msla/merged/h/ in two-month delayed time and can be automatically downloaded. The SL data also need to be interpolated to the model grid and monthly time scale.

#### Research on GODAE/GHRSST

#### The research on high-resolution SST merging in northwest Pacific Ocean using satellite SST data from AVHRR and AMSR-E etc. has been carried out at Ocean Remote Sensing Institute (ORSI) of Ocean University of China (OUC) (Guan et al. 2008, 2006, 2005, 2004). The objective analysis, wavelet transform and feature tracking technique are used to merge data, and the fine oceanic structures such as fronts and eddies are better preserved by the latter method. The input data are AVHRR and AMSR-E SST products. The AVHRR SST products are acquired through the satellite ground station in Ocean University of China (http://www.station.ouc.edu.cn), and the SST products are processed in near real-time. The AMSR-E SST products are produced by the American Remote Sensing Systems company (http://www.remss.com/). The development of an operational system used to process and distribute Chinese regional high resolution SST products in the China Seas is funded by a national 863 ocean project in China.

#### Monitoring the floating algae by MODIS data in Qingdao Olympic sailing area  in 2008

#### Extensive patches of floating algae (Enteromorpha prolifera) appeared in coastal waters off Qingdao in early June on the eve of 2008 Qingdao Olympic sailing competitions. In order to ensure the training of the sailors from more than 30 countries in Qingdao coastal area, the Qingdao government set up an emergency management office and called on citizens to clear up the floating algae. The ORSI of OUC played an important role in monitoring the floating algae utilizing satellite data. The distribution, coverage extent, evolution and origin of the floating algae in coastal area near Qingdao are observed and analyzed using MODIS RGB and NDVI time-series data (Hu and He et al., 2008). National Satellite Ocean Application Service (NSOAS) and North China Sea Branch (NCSB) of State Oceanic Administration (SOA), Institute of Remote Sensing Applications (IRSA) and Remote-Sensing Satellite Ground Station (RSGS) of Chinese Academy of Sciences (CAS) also used MODIS RGB data to monitor floating algae in coastal area near Qingdao.

#### In above three application cases, some international satellite data products are utilized. However, how to utilize Chinese satellites data for ocean applications is an important issue and further investigations need to be done.

Reference：

FY-n ：    http://www.cma.gov.cn/

http://nsmc.cma.gov.cn/

http://www.gmss.cn

http://61.232.252.2/

HY-n ：    http://www.soa.gov.cn/

http://www.nsoas.gov.cn

ZY-n ：    http://www.cresda.com/cn/

DMC/BJ-1：http://www.blmit.com.cn/

HJ-n ：    http://www.jianzai.gov.cn/rs/

http://www.cresda.com/cn/

SZ-n ：    http://www.cas.ac.cn/

http://www.cnsa.gov.cn/

CRS-n ：   http://www.gov.cn/

http://www.cnsa.gov.cn/

http://www.cas.ac.cn/

IOCCG     http://www.ioccg.org/sensors/current.html ;

WMO      http://www.wmo.ch/pages/prog/sat/GOSresearch.html;

CEOS      http://www.eohandbook.com/eohb05/ceos/part3_3.html

JCOMM    http://www.jcomm.info/

NASA      http://www.nasa.gov/

JPL        http://www.jpl.nasa.gov/

GSFC      http://www.gsfc.nasa.gov/

ESA       http://www.esa.int/

CNES      http://www.cnes.fr/

DLR       http://www.dlr.de/en/

CSA       http://www.space.gc.ca/

JAXA      http://www.jaxa.jp/

Deren Li. Chinese Earth Observation Missions. ESA-MOST Dragon 1 final results and Dragon 2 kick-off symposium. Beijing, 21 April 2008.

http://dragon2.esa.int/symposium2008/dr2_ppts/4_21/li_deren.pdf

Delu Pan. Present and future Chinese satellite missions for ocean remote sensing. ESA-MOST Dragon 2nd Advanced Training Course. Hangzhou 15-20 Oct. 2007.

http://earth.esa.int/dragon/ocean_training/Lecture_Material/DAY1-15Oct2007/D1_L1_Pandelu_lectur_20071015_V1.pdf

Xingwei Jiang. Satellite ocean exploration of space in China. Presentation at Ocean University of China. Qingdao, Jan. 2008. http://www.ouc.edu.cn/

Acronyms and Abbreviations:

| ADEOS | Advanced Earth Observing Satellite |
| --- | --- |
| AFRL | Air Force Research Laboratory |
| ALDIN | Atmospheric Laser Doppler INstrument |
| AMSR-E | Advanced Microwave Scanning Radiometer - EOS |
| APS | Aerosol Polarimeter Sensor |
| ASAR | Advanced Synthetic Aperture Radar |
| AVHRR | Advanced Very High Resolution Radiometer |
| CAS | Chinese Academy of Sciences |
| CBERS | China-Brazil Earth Resources Satellite |
| CEOS | Committee on Earth Observation Satellites |
| CMA | China Meteorological Administration |
| CNES | Centre National d’Etudes Spatiales |
| CNSA | China National Space Administration |
| COCTS | Chinese Ocean Color and Temperature Scanner |
| COMS | Communication, Ocean, Meteorological Satellite |
| CSA | Canadian Space Agency |
| CZCS | Coastal Zone Color Scanner |
| CZI | Coastal Zone Imager |
| DLR | German Aerospace Centre |
| DMC | Disaster Monitoring Constellation |
| ENSO | El Niño - Southern Oscillation |
| EOS | Earth Observing System |
| EPS | Ensemble Prediction System |
| ERM | Earth Radiation Measurement |
| ESA | European Space Agency |
| EUMETSAT | European Organization for the Exploitation of Meteorological Satellites |
| EVA | Extra-Vehicular Activity |
| GHRSST | GODAE High Resolution Sea Surface Temperature |
| GNSS | Global Navigation Satellite System |
| GOCI | Geostationary Ocean Color Imager |
| GODAE | Global Ocean Data Assimilation Experiment |
| GRAS | GNSS Receiver for Atmospheric Sounding |
| GSFC | Goddard Space Flight Center |
| HICO | Hyperspectral Imager for the Coastal Ocean |
| HR | High Resolution camera |
| HSI | Hyper Spectral Imager |
| I I S | Interferometric Infrared Sounder |
| IOCCG | International Ocean Colour Coordinating Group |
| IRAS | Infrared Atmospheric Sounder |
| IRMSS | Infrared Multi-Spectral Scanner |
| IRSA | Institute of Remote Sensing Applications |
| ISS | International Space Station |
| JAXA | Japan Aerospace Exploration Agency |
| JCOMM | Joint WMO-IOC Technical Commission for Oceanography and Marine Meteorology |
| JEM | Japanese Experiment Module |
| JPL | Jet Propulsion Laboratory |
| LM | Lightning Mapper |
| MCA | Ministry of Civil Affairs |
| MCSI | Multiple Channel Scanning Imager |
| MEP | Ministry of Environmental Protection |
| MERIS | MEdium Resolution Imaging Spectrometer |
| MERSI | MEdium Resolution Spectral Imager |
| MLR | Ministry of Land and Resources |
| MODIS | Moderate Resolution Imaging Spectroradiometer |
| MOST | Ministry of Science and Technology |
| MVISR | Multichannel Visible Infrared Scanning Radiometer |
| MWHS | MicroWave Humidity Sounder |
| MWRI | MicroWave Radiation Imager |
| MWTS | MicroWave Temperature Sounder |
| NASA | National Aeronautics and Space Administration |
| NCSB | North China Sea Branch |
| NDVI | Normalized Difference Vegetation Index |
| NIST | National Institute of Standards and Technology |
| NOAA | National Oceanic and Atmospheric Administration |
| NPOESS | National Polar-orbiting Operational Environmental Satellite System |
| NRL | Naval Research Laboratory |
| NSOAS | National Satellite Ocean Application Service |
| OCI | Ocean Color Imager |
| OCTS | Ocean Color and Temperature Scanner |
| ORSI | Ocean Remote Sensing Institute |
| OUC | Ocean University of China |
| PAN-MUX | Panchromatic and Multi-spectral camera |
| SBUS | Solar Backscatter Ultraviolet Sounders |
| SST | Sea Surface Temperature |
| SeaWiFS | Sea-viewing Wide Field-of-view Sensor |
| SEM | Space Environment Monitors |
| SIM | Solar Irradiation Monitor |
| SOA | State Oceanic Administration |
| TOU | Total Ozone Unit |
| TOVS | TIROS Operational Vertical Sounder |
| TMI | TRMM Microwave Imager |
| TRMM | Tropical Rainfall Measuring Mission |
| VIRR | Visible and InfraRed Radiometer |
| VISSR | Visible and Infrared Spin Scan Radiometer |
| WFI | Wide Field Imager |
| WMO | World Meteorological Organization |

Acknowledgements

This study is supported by EU FP6 DRAGONESS Project (No. SSA5–CT–2006- 030902) and ESA-MOST Dragon Programme Ocean Project (ID2566). Thanks to Qian Yang, Yili Zhao, Lei Zhang and Ning Li for participating in the investigation of DRAGONESS WP2 Project.

# Text boxes

DRAGONESS DRAGONESS